## Slide 1
http://www.youtube.com/watch?v=3EeJCln5KYg

## Slide 2: Robotics
CS311, Spring 2013
David Kauchak
Some material adapted from slides from Zach Dodds

## Slide 3: Admin
Assignment 5 graded
Exam #2 available later today
  To be done by Sunday at midnight

## Slide 4: What is a robot?
"I can't define a robot, but I know one when I see one.”
--Joseph Engelberger (1966)
Justice Potter Stewart wrote in Jacobellis v. Ohio (1964), "I can't define pornography, but I know it when I see it."
Notes: Joseph Engelberger has been called the father of robotics. The American engineer and entrepreneur helped create the first industrial robot. In 1966, he appeared on The Tonight Show with Johnny Carson along with a robot that served a beer, sunk a putt and led the band. Asked to define a robot, he once said, "I can't define a robot, but I know one when I see one."

## Slide 5: Robot Defined
Word robot was coined by a Czech novelist Karel Capek in a 1920 play titled Rossum’s Universal Robots (RUR)
Robota in Czech is a word for worker or servant
Definition of robot:
  Any machine made by one our members: Robot Institute of America 
  A robot is a reprogrammable, multifunctional manipulator designed to move material, parts, tools or specialized devices through variable programmed motions for the performance of a variety of tasks: Robot Institute of America, 1979
Karel Capek

## Slide 6
What is a Robot
Manipulator

## Slide 7
What is a Robot
Wheeled Robot
Legged Robot

## Slide 8
What is a Robot
Unmanned Aerial Vehicle
Autonomous Underwater Vehicle

## Slide 9
Robot Plot
Bar Monkey (9)
Roomba (7)
Genghis (3)
Stanford Cart (3)
Shakey (3)
MERs (8)
Sims (5)
Capability (0-10)
Stanley/Boss (9)
Autonomy
human-controlled
independent
less
World Modeling
more
Unimate (4)
da Vinci (2)

## Slide 10
Robot timeline?
...
1921
2421
2150
2020
1950

## Slide 11
Fictional Robot timeline
...
1921
2421
2150
2020
Put these robots in chronological order?
Notes: protectors and terminators
as well as _ex_terminators…

## Slide 12
Fictional robot timeline
...
1921
2421
2150
2020
1950
I, Robot
Karl Capek
Rossum’s Universal Robots
Asimov
Notes: exterminate all humans sound <- mac iTunes
robots: need to be freed from their work! RUR

## Slide 13
Real robot timeline
...
1951
1968
1976
1985

## Slide 14
Real robot timeline
...
1951
Tortoise “Elsie”
by Neurophysiologist Grey Walter
http://www.frc.ri.cmu.edu/~hpm/talks/revo.slides/1950.html

## Slide 15
Shakey
Nils Nilsson @ Stanford Research Inst.
...
...
1968
first “general-purpose” mobile platform
Living Room (L)
rem
sp
Kitchen (K)
Bedroom (B)
sh
tv

## Slide 16
Go(from,to)
Preconditions: At(sh,from)
Postconditions: At(sh,to)
Push(obj,fr,to)
Preconditions: At(sh,fr)  At(obj,fr)
Postconditions: At(sh,to)  At(obj,to)
Robotics's Shakey start
START
GOAL
ACTIONS
Go(L,B)
Go(L,K)
At(sh,L)  At(sp,K)  At(rem,B)  At(tv,L)
Push(tv,L,B)
Push(tv,L,K)
At(sh,K)  At(sp,K)  At(rem,B)  At(tv,K)
At(sh,L)  At(sp,L)  At(rem,L)  At(tv,L)
Notes: STRIPS planning
explicit representation of high-level environmental states…
-- low-level engineering of actuation and control had to be improved
- -algorithms for reasoning about the robot's environment had to be improved
VIDEO!

## Slide 17: Shakey in video
http://www.youtube.com/watch?v=qXdn6ynwpiI

## Slide 18
Stanford Cart: SPA
Hans Moravec @ SAIL
...
...
1976
SENSING
ACTING
perception
world modeling
Planning
task execution
motor control
“functional” task decomposition
“horizontal” subtasks
Notes: The field moved slowly, mostly because computation moved slowly!

## Slide 19
Cartland (outdoors)

## Slide 20
Cartland (indoors)

## Slide 21
“Robot Insects”
Rodney Brooks @ MIT
...
...
1985
avoid objects
wander
explore
build maps
identify objects
planning and reasoning
SENSING
ACTING
“behavioral” task decomposition
“vertical” subtasks
Notes: picture of Rodney Brooks – his paper!!

## Slide 22: Robotics
What are the challenges?
How do these relate to AI?

## Slide 23: AI
Search
  planning
Game playing
CSPs
Bayesian
HMMs
Machine learning
  neural nets
Knowledge representation
Natural Language processing
Computer vision

## Slide 24
how much of the world do we need to represent internally ?
how should we internalize the world ?
what outputs can we effect ?
what inputs do we have ?
what algorithms connect the two ?
how do we use this “internal world” effectively ?
Autonomy/behavior
Robot Architecture

## Slide 25
Robot Architecture
how much / how do we represent the world internally ?
Task-specific
Not at all
As much as possible!
Reactive paradigm
SPA paradigm
Behavior-based architecture
As much as possible.
Hybrid approaches
sense
plan
act
history…
Notes: historically, this has come full circle!

## Slide 26
Sense - Plan - Act
...
...
1976
SENSING
ACTING
perception
world modeling
planning
task execution
motor control
sense
plan
act
Stanford Cart
Shakey
1968
MERs
… - 2009
Notes: Shakey video

## Slide 27
Mars Exploration Rovers
Sense – Plan – Act "deliberative" architecture
Mars Science Lab
2011 - lasers, lifebio, and maybe nuclear-powered
Notes: Video!

## Slide 28
Robot Architecture
how much / how do we represent the world internally ?
Task-specific
Not at all
As much as possible!
Reactive paradigm
SPA paradigm
Behavior-based architecture
As much as possible.
Hybrid approaches
sense
plan
act
sense
act
stimulus - response

## Slide 29
Biological Inspiration
Ethology: describing animal behavior
Getting to the ocean?
AI reasoning systems abstract too much away: frame problem
sense
act
Decision-making is based only on current sensor inputs.
“The world is its own best model”
Digger wasps’ nest-building sequence
Notes: Some Sphex wasps drop a paralyzed insect near the opening of the nest. Before taking provisions into the nest, the Sphex first inspects the nest, leaving the prey outside. During the inspection, an experimenter can move the prey a few inches away from the opening. When the Sphex emerges from the nest ready to drag in the prey, it finds the prey missing. The Sphex quickly locates the moved prey, but now its behavioral "program" has been reset. After dragging the prey back to the opening of the nest, once again the Sphex is compelled to inspect the nest, so the prey is again dropped and left outside during another stereotypical inspection of the nest. This iteration can be repeated again and again, with the Sphex never seeming to notice what is going on, never able to escape from its programmed sequence of behaviors.

## Slide 30
Analog reactive robots
...
1951
“Tortoise”
Gray Walter
1984
“BEAM”
Mark Tilden
“light-headed” behavior
stateless...
http://people.cs.uchicago.edu/~wiseman/vehicles/
1989-
Valentino Braitenberg
robot made from Playstation pieces…!
http://haroldsbeambugs.solarbotics.net/mercury.htm
commercial products…
Notes: BEAM == Biology, Electronics, Aesthetics, and Mechanics
http://people.cs.uchicago.edu/~wiseman/vehicles/

## Slide 31
Robot Architecture
how much / how do we represent the world internally ?
Task-specific
Not at all
As much as possible!
Reactive paradigm
SPA paradigm
Subsumption paradigm
Potential Fields
Behavior-based architecture
As much as possible.
Hybrid approaches
sense
plan
act
sense
act
different ways of composing behaviors
stimulus – response == "behavior"

## Slide 32
...
...
1985
avoid objects
wander
explore
build maps
identify objects
planning and reasoning
SENSING
ACTING
Genghis
“Vertical” task decomposition
sense
act
little explicit deliberation except through system state
Behavior-based control
Behavior
a direct mapping of sensory inputs to a pattern of task-specific motor actions
extinguish
approach
wander

## Slide 33
Subsumption
Subsumption builds intelligence incrementally in layers
runaway behavior
wander behavior

## Slide 34
Subsumption
Where would a light-seeking behavior/layer connect?
runaway behavior
wander behavior

## Slide 35
Subsumption
Where would a light-seeking behavior/layer connect?
runaway behavior
wander behavior
S
Closest Light
LIGHT
SONAR
phototaxis

## Slide 36
Subsumption - Limits
Success of behavior-based systems depends on how well-tuned they are to their environment. This is a huge strength, but it's also a weakness …
Herbert, a soda-can-collecting robot
Reaching the end of the subsumption architecture and purely reactive approaches.
http://www.youtube.com/watch?v=YtNKuwiVYm0

## Slide 37
Subsumption limits: Genghis
runaway behavior
wander behavior
navigate behavior
FSM / DFA

## Slide 38
Unwieldy!
Larger example -- Genghis
1) Standing by tuning the parameters of two behaviors: the leg “swing” and the leg “lift”
2) Simple walking: one leg at a time
3) Force Balancing: via incorporated force sensors on the legs
4) Obstacle traversal: the legs should lift much higher if need be
5) Anticipation: uses touch sensors (whiskers) to detect obstacles
6) Pitch stabilization: uses an inclinometer to stabilize fore/aft pitch
7) Prowling: uses infrared sensors to start walking when a human approaches
8) Steering: uses the difference in two IR/range sensors to follow
57 modules wired together !

## Slide 39
Robot Architecture
how much / how do we represent the world internally ?
Task-specific
Not at all
As much as possible!
Reactive paradigm
SPA paradigm
Subsumption paradigm
Potential Fields
Behavior-based architecture
As much as possible.
Hybrid approaches
sense
plan
act
sense
act
different ways of composing behaviors

## Slide 40
Potential Fields
Potential fields compose simple behaviors by adding the outputs that each sensor/input sends the robot
Ron Arkin @ Georgia Tech
A sequencing process (FSM/DFA) updates the potential fields and/or decides which ones to run next…
Individual potential fields (motor schemas) contain state

## Slide 41
Motor Schemas / Potential Fields
goal-seeking schema
obstacle-avoiding schema
note that the complete environmental vector fields are only for visualization!
Direct mapping from the environment to a control signal
combine?

## Slide 42
Behavior Summer
vector sum of the avoid and goal motor schemas
path taken by a robot controlled by the resulting field

## Slide 43
Implementation details
the extent to which potential field force drops off with distance…
corridor-following schema(s)?
what crucial assumption is being made here?
Notes: Crucial assumption: that the robot KNOWS the potential field
sensor networks or significant sensing challenge!

## Slide 44
Additional behavior primitives
go! schema
corridor-centering schema

## Slide 45
A more complex task
Direct mapping from the environment to a control signal
larger composite task
How many individual fields are summed in this task?
Not necessarily all at one time!
Notes: 5 or 6 vector fields here

## Slide 46
Local minima
A potential-field-based system can get stuck!
the problem
a solution?
What would happen if a robot came in in the middle on the left?

## Slide 47
Local minima
A potential-field-based system can get stuck!
the problem
Why is the “local minimum” problem, as illustrated to the left, not likely to actually cause a robot to get stuck in practice?
robots controlled by summing goal/obstacle potential fields can get stuck in practice -- draw an example of an environment with both obstacle(s) and goals(s) in which getting stuck might actually occur.
Suggest how a robot might overcome the problem of getting stuck in such cases…

## Slide 48
Local minima
A potential-field-based system can get stuck!
the problem
a solution

## Slide 49
Bigger deadends...
How to get out of larger wells ?

## Slide 50
Bigger deadends...
uses memory of where the robot has been
past-avoiding motor schema

## Slide 51
Another example
Keeping away from past locations...

## Slide 52
Pfields in Practice
Steathy navigation @ USC (Ashley Tews, Gaurav S. Sukhatme, and Maja J. Mataric)
part of the potential field… What's going on here?
http://robotics.usc.edu/interaction/?l=Research:Projects:stealth:index#experiments
Notes: red == observer we want to avoid
yellow == goal
blue == robot
obstacles cast "unobservable shadows"
show Lec2/usc_pfields_exp1_r1.mov

## Slide 53
Docking with potential fields
How does the idea of docking, e.g., with an electrical outlet change the requirements for a potential field?
example goals
Why might a simple attractive force not be sufficient for docking (plugging-in, etc.)?

## Slide 54
Docking with potential fields
The key insight is the need to establish an approach direction
example goals

## Slide 55
Docking with potential fields
The key insight is the need to establish an approach direction

## Slide 56: Review
Machine learning
  general learning concepts
    supervised vs. unsupervised
    features/feature-based problems/feature space
    bias/variance
    overfitting
    hyperplanes/linear seperability
  Supervised learning
    applications
    approaches
      k-NN
      decision trees
      NB
      SVM (large margin classifiers)
    Ensemble approaches (boosting)

## Slide 57: Review
Machine learning (continued)
  unsupervised learning
    application
    issues
      number of clusters
      flat vs. hierarchical
      soft vs. hard clustering
    approaches
      k-means
      EM
        word alignment
        clustering (mixture of gaussians)
      spectral clustering (min-cut)

## Slide 58: Review
Neural networks (Machine learning?)
  perceptrons/neurons
    activation functions (threshold vs. sigmoid)
    perceptron learning
  multi-layer networks
Knowledge representation
  basic logic
  ontology
  NELL

## Slide 59: Review
CSPs
  problem formulation
    variables
    domain
    constraints
  why CSPs? applications?
  constraint graph
  CSP as search
    backtracking algorithm
    forward checking
    arc consistency
  heuristics
    most constrained variable
    least constrained value
    ...

## Slide 60: Review
Natural language processing
  Applications
  Problem areas
  Why it’s hard?
  Machine translation setup

## Slide 61: Guest speaker
Rodney Brooks
  Professor at MIT (was previous director of CSAIL)
  Founder of iRobot
http://www.youtube.com/watch?v=B79D9nW2AFA